## Slide 1: Tissue clearing
When a sample is surrounded by a medium with a different refractive index, light suffers multiple events scattering, therefore it appears opaque
If instead the sample and the surrounding medium share the same refractive index, no scattering occurs and light traverses the specimen unhindered. This causes the sample to appear transparent
Biological tissues are characterize from the presence of macro-molecules like proteins and lipid bilayers with different refractive index that make the clearing more difficult

## Slide 2: Tissue clearing
There are two different approaches to clear the brain:
Replace the water inside the tissue with a solvent (organic or aqueous) with the same proteins’ refractive index (chemical clearing)
Transform the brain into a nanoporous hydrogel-protein-hybridized lipid free form that is optically transparent and macromolecule-permeable (CLARITY)
Uncleared
Cleared

## Slide 3: CLARITY
[Chung et al. Nature 2013]
Step 1: formaldehyde crosslinks the tissue and the hydrogel monomers to proteins
Step 2: polymerization of the biomoleculeconjugated monomers into a hydrogel mesh
Step 3: extraction of the lipids with ETC
Step 4: refractive-index matching and imaging: usually FocusClear is used, which is a aqueous solvent extremely expensive (20$/ml). Each experiment might cost up to 2000 $

## Slide 4: Optical clearing
Biological tissues are opaque because of light scattering, the refractive index of proteins is very different from that of water
To clear the tissues is necessary to replace the water inside the brain with a solvent (organic or aqueous) with the same proteins’ refractive index
Uncleared brain
Organic solvent (RI=1.56)
Aqueous solvent (RI=1.42)
THF + DBE
TDE
Uncleared slide 1mm
THF= tetrahydrofuran; DBE= dibenzyl ether; TDE= thiodiethanol

## Slide 5: CLARITY
[Chung et al. Nature 2013]
CLARITY is a method for the transformation of intact tissue into a nanoporous hydrogel-hybridized lipid free form that is fully assembled but optically transparent and macromolecule-permeable

## Slide 6: Connectomics protocol
Transgenic animals
GFPM
Mounting
Tomography and image analysis
Preparation
Dehydration
Clearing